# SEP #81: Introduction of eigs function

Version: 1.0
Author: Adeline CARNIS
Review:
Commented:
State:
Scilab-Version: 5.4.0
Created: 18 April 2012

## Abstract
Eigs calculates eigenvalues and eigenvectors of matrix.

## Rationale
d = eigs(A) solves the eigenvalue problem A*v = lambda*v. This calling returns a vector of A's six largest magnitude eigenvalues. A is either a square matrix, which can be symmetric or non-symmetric, real or complex, full or sparse, or a function.

- [d, v] = eigs(A) returns a diagonal matrix D of A's six largest magnitude eigenvalues and a matrix V whose columns are the corresponding eigenvectors.
- eigs(A, B) solves the generalized eigenvalue problem A*v = lambda*B*V. So,
  - if B is not specified, B = [] is used.
  - if B is specified, B must be the same size as A.
- eigs(A, B, k) return the number of eigenvalues desired. If k is not specified, k=min(n,6).

- eigs(A, B, k, sigma) return k eigenvalues on sigma. Sigma can be either scalar or string.
  - Scalar: sigma can be real, complex including 0.
  - String: if sigma is one the followings strings, it specifies the desired eigenvalues:
    - 'LM': largest magnitude (by default).
    - 'SM': smallest magnitude (same as sigma = 0). If A is a function, it must return y = A\x.
    - 'LA': largest algebraic
    - 'SA': smallest algebraic
    - 'LR': largest real part
    - 'SR': smallest real part
    - 'LI': largest imaginary part
    - 'SI': smallest imaginary part

- eigs(A, B, k, sigma, opts) specify an options structure.
  - opts.tol (scalar): convergence: Ritz estimate residual <= tol*norm(A). by default, tol = eps.
  - opts.maxiter (integer): maximum number of iterations. By default, maxiter = 300.
  - opts.ncv (integer): number of Lanczos basis vectors. By default, p = 2*k.
  - opts.resid (n by 1 vector): starting vector. By default, resid = rand(n,1)-0,5
  - opts.chol: 1 if B is really its Cholesky factor chol(B), 0 otherwise. By default 0.
  - opts.perm: permutation vector perm if sparse B is really chol(B(perm, perm)). By default {1:n}.

If A is a function, it should return:
- A*x	if sigma is not specified, or is a string other than 'sm'.
- A\x	if sigma is 0 or 'sm'.
- (A-sigma*I)\x	if sigma is a nonzero scalar (standard eigenvalue problem).
- (A-sigma*b)\x	if sigma is a nonzero scalar (generalized eigenvalue problem).

## Example
// A is a symmetric real matrix:
A = diag(10*ones(10,1)); / A(1:$-1,2:$) = A(1:$-1,2:$) + diag(6*ones(10-1,1)); / A(2:$,1:$-1) = A(2:$,1:$-1) + diag(6*ones(10-1,1)); / eigs(A) / 21.5139 / 20.0950 / 17.8583 / 14.9850 / 11.7078 / 8.2922 / eigs(A, eye(10,10), 8,'SM') / ans = / 17.858329 / 14.98498 / 11.707778 / 8.2922219 / 5.0150198 / 2.1416712 / - 0.0950424 / - 1.5139157

// A is non-symmetric real matrix:

A = diag(10*ones(10,1)); / A(1:$-1,2:$) = A(1:$-1,2:$) + diag(6*ones(10-1,1)); / A(2:$,1:$-1) = A(2:$,1:$-1) + diag(-6*ones(10-1,1)); / eigs(A) / eigs(A, eye(10,10), 8, 'SM')

// A is a non-symmetric complex matrix:

A = diag(10*ones(10,1)+%i*ones(10,1)); / A(1:$-1,2:$) = A(1:$-1,2:$) + diag(6*ones(10-1,1)); / A(2:$,1:$-1) = A(2:$,1:$-1) + diag(-6*ones(10-1,1)); / eigs(A) / eigs(A, eye(10,10), 8, 'SM')

### Bibliography
http://www.mathworks.fr/help/techdoc/ref/eigs.html
### Changelog
1.0 – Initial Version
### Copyright
This document has been placed under the license CeCILL-B.